## Slide 1: IP-TFS
Christian Hopps
LabN Consulting, LLC

## Slide 2: Key Design Points
Improves on existing IPsec solution
Unidirectional (like IPsec)
Constant send rate, Fixed packet size
Congestion Controlled and Non-CC operating modes
Uses IPsec
[Optional] Uses IKEv2
Minimize configuration required

## Slide 3: Unidirectional/Bidirectional
Data path is unidirectional
  Sender to Receiver
Congestion-Control (CC) info is sent in reverse direction
  Receiver to Sender
Configure 2 paths for bidirectional operation

## Slide 4: Constant Send Rate/Fixed Packet Size
Packet size never varies
Packet size manual or automatic configuration
Use Path MTU Discovery for automatic optimal configuration
Constant send rate
Provides requisite transport flow confidentiality

## Slide 5: Variation Fully Allowed
Egress must accept packets at any rate.
Egress must accept packets of any size.
IPSec tunnels can start in normal "IP Mode" and transition to IP-TFS.
  SA reset required to leave IP-TFS mode.

## Slide 6: Congestion Controlled (CC) Mode
Send rate (PPS) adjusted, packet size fixed
  Congestion causes packet drops not byte drops
CC Info sent from Receiver to Sender in IKEv2 notification data.
Sender uses congestion control algorithms to modify packet send rate.
CC algorithm a local choice
  No need to standardize
Circuit breaking supported.
ECN supported but off by default.

## Slide 7: Non-Congestion-Controlled Mode
For use when IP path bandwidth can be guaranteed.
Packet loss reported by receiver to admin/operations.
Optional CC info can be used to report packet loss from sender.
Optional CC info can be used for circuit breaker.

## Slide 8: IPSec Transport
Use IPSec/ESP (encrypted encapsulation) as transport
Input packets are fragmented and aggregated into IPSec/ESP packet stream
New IP Protocol Number for new ESP payload (framing)

## Slide 9: IKEv2 (CC Info)
Use IKEv2 for CC info advertisement
Use INFORMATION "exchange" Notification Data
Periodic send interval (e.g., 1 per second)
Non-reliable transport (I.e., not a REQUEST/RESPONSE exchange)
CFG_REQUEST/CFG_REPSPONSE used to configure interval.
0 interval allowed for no send.

## Slide 10: IP-TFS Packet Format
. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
. Outer Encapsulating Header ... .
. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
. ESP Header... .
+-----------------------------------------------------------------+
|V| Reserved | BlockOffset |
+-----------------------------------------------------------------+
| Data Blocks Payload ... ~
~ |
+-----------------------------------------------------------------|
. ESP Trailer... .
. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

## Slide 11: ESP Payload Format
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|V| Reserved | BlockOffset |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DataBlocks ...
+-+-+-+-+-+-+-+-+-+-+-
V :: Version, must be set to zero and dropped if set to 1.
Reserved :: set to 0 ignored on receipt.
Block Offset :: This is the number of bytes before the next IP/IPv6 data block. It can point past the end of the containing packet in which case this packet is the continuation of a preivous one and possibly padding. NOTE: This can point into the next packet and yet the current packet can end with padding. This will happen if there's not enough bytes to start a new inner packet in the current outer packet.
Data Blocks :: variable number of bytes that constitute the start or continuation of a previous data block.

## Slide 12: Data Blocks
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | IPv4, IPv6 or pad...
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-
Version
  0x0 for pad
  0x4 for IPv4
  0x6 for IPv6.

## Slide 13: IPv4 Data Blocks
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 0x4 | IHL | TypeOfService | TotalLength |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Rest of the inner packet ...
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-
Version :: 0x4 for IPv4
Total Length :: Length of the IPv4 inner packet.

## Slide 14: IPv6 Data Blocks
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 0x6 | TrafficClass | FlowLabel |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| TotalLength | Rest of the inner packet ...
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-
Version :: 0x6 for IPv6
Total Length :: Length of the IPv4 inner packet.

## Slide 15: Pad Data Blocks
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 0x0 | Padding ...
+-+-+-+-+-+-+-+-+-+-+-
Version :: 0x0 for Padding
Padding :: extends to end of the encapsulating packet.

## Slide 16: IKEv2 Config CC Info Sending Interval Attribute
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|R| Attribute Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Interval |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
R:: 1 bit set to 0
Attribute Type:: 15 bit value set to TFS_INFO_INTERVAL (TBD).
Length:: 2 octet length set to 2.
Interval :: 2 octet unsigned integer. The sending interval in milliseconds.

## Slide 17: CC Info Notification Data
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|E| Reserved | DropCount |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| AckSeqStart |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| AckSeqEnd |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
E :: A 1 bit value that if set indicates that packet[s] with Congestion Experienced (CE) ECN bits set were received and used in calculating the DropCount value.
Reserved :: set to 0 ignored on receipt.
DropCount:: For ack data block this is the drop count between AckSeqStart and AckSeqEnd, If the drops exceed the resolution of the counter then set to the max value.
Timestamp :: The time when this notification was created and sent.
AckESPSeqStart :: The first ESP Seq. Num. of the range that this information relates to.
AckESPSeqEnd :: The last ESP Seq. Num. of the range that this information relates to.

## Slide 18: Local Config – Reordering Window
IPsec packets can arrive out of order
Number of packets allowed missing prior from received newest packet (by seqno)
So if window is 3 and we receive 3, 5, 2, 1:
  3 waits on 1 and 2
  5 waits on 4 (3 ok)
  2 is in window and on edge so handled immediately then 3 as well.
  1 is dropped as > 3 from 5
Reordering window size is a local configuration option

## Slide 19: Local Config – Max Latency
Max latency – ammount of time a last byte of packet waits to be sent.
Max send latency (worst case) Is outqsz * max input packet size
Ingress input queue can track byte counts an using output rate determine latency.
Mode-3 drops if max latency is reached.
Mode-2 enqueues packet enters "fast mode"

## Slide 20: Mode 2 (allow for burst)
Max latency in queue is exceeded
Send IP-TFS tunnel packets faster than normal rate until queue is below max-latency.
If we are congestion controlled this is probably not smart.
Mode-2.5?
  Allow enqueues to exceed max-latency, but do not send IP-TFS packets faster.

## Slide 21: Backup Slides

## Slide 22: Overhead of bytes per inner packet.
| Type | IPSec | IPSec | IPSec | TFS | TFS | TFS |
|PktSize| 576 | 1500 | 9000 | 576 | 1500 | 9000 |
|------+-------+-------+-------+-------+-------+------|
| 64 | 512 | 1436 | 8936 | 4.8 | 1.8 | 0.3 |
| 128 | 448 | 1372 | 8872 | 9.6 | 3.5 | 0.6 |
| 256 | 320 | 1244 | 8744 | 19.1 | 7.0 | 1.1 |
| 536 | 40 | 964 | 8464 | 40.0 | 14.7 | 2.4 |
| 576 | 600 | 924 | 8424 | 43.0 | 15.8 | 2.6 |
| 1460 | 312 | 40 | 7540 | 109.0 | 40.0 | 6.5 |
| 1500 | 272 | 1524 | 7500 | 111.9 | 41.1 | 6.7 |
| 8960 | 560 | 144 | 40 | 668.7 | 245.5 | 40.0 |
| 9000 | 520 | 1624 | 9024 | 671.6 | 246.6 | 40.2 |

## Slide 23: Overhead as percentage of inner packet.
| Type | IPSec | IPSec | IPSec | TFS | TFS | TFS |
| MTU | 576 | 1500 | 9000 | 576 | 1500 | 9000 |
|------+--------+---------+----------+------+------+------|
| 64 | 800.0% | 2243.8% | 13962.5% | 7.5% | 2.7% | 0.4% |
| 128 | 350.0% | 1071.9% | 6931.2% | 7.5% | 2.7% | 0.4% |
| 256 | 125.0% | 485.9% | 3415.6% | 7.5% | 2.7% | 0.4% |
| 536 | 7.5% | 179.9% | 1579.1% | 7.5% | 2.7% | 0.4% |
| 576 | 104.2% | 160.4% | 1462.5% | 7.5% | 2.7% | 0.4% |
| 1460 | 21.4% | 2.7% | 516.4% | 7.5% | 2.7% | 0.4% |
| 1500 | 18.1% | 101.6% | 500.0% | 7.5% | 2.7% | 0.4% |
| 8960 | 6.2% | 1.6% | 0.4% | 7.5% | 2.7% | 0.4% |
| 9000 | 5.8% | 18.0% | 100.3% | 7.5% | 2.7% | 0.4% |

## Slide 24: Questions and Comments
More pictures of aggregated inner packets in outer.